## Slide 2: What does it mean to be the same as something else?
100, 100.001
If you set a tolerance of 0.005 – these are the same
(100.001-100<0.005)
100.000, 100.001, 100.002, 100.003, 100.004, 100.005, 100.006
Complexity of calculation grows exponentially as each value must be compared to each other (n2 calculation)
100.006 would typically be classed with 100.000 by a technician knowing that there is some degree of instrument “drift” across a run which is acceptable

## Slide 3: Peak alignment algorithm
CCS – typically 2%
RT – typically 1 minute
m/z – typically 0.001%
All user defined parameters depending on the performance of the instrument
Uses DBSCAN – to my knowledge this is the first application to MS of this algorithm – exceptionally fast
Cluster 1
Isolated point

## Slide 4: Something potentially novel? Maybe
m/z
9ppm
Within margin of error
81ppm- points still classed as being in the same “cluster”
Results in anomalously large clusters – features which aren’t related are grouped together due to this drifting effect
However, instrument performance is known to gradually change with time – it rarely remains within the tolerance for the entire run requiring manual intervention (tuning, recalibration)

## Slide 5: Drift tolerance
m/z
Median value calculated
Drift tolerance
(user defined integer * maximum point to point tolerance)
Points defined as noise now

## Slide 6: In action
12.7% min-max spread
4.6% min-max spread
Totally user defined based on instrument performance
Good for things like SLIMS with known drift
1.2 drift tolerance