## Slide 1: Alligator PFAS Study: Non-Targeted Analysis
December 2024

## Slide 2: Background
5 years (2018-2022), 4 sites (3 NC + 1 FL), ~200 samples
Big Questions
  What type and how much PFAS are in alligator plasma?
    Absolute quant of up to 26 PFAS
      Output: ng/ml PFAS in plasma
    Target screening of ~100 PFAS in library
      Output: detect yes/no
      Output: relative abundance
    Non-targeted analysis to find additional PFAS in plasma
  Can we fingerprint year and site using PFAS in alligator plasma?
    Input: ng/ml PFAS in plasma (Sum26 PFAS and sum6 regulated PFAS)
    Input: relative abundance (if detected in enough individuals for each group)
    Input: detection frequency of each PFAS
  Are any PFAS associated with health endpoints for the alligators?

## Slide 3: Experimental Design
Extract 200 plasma samples along with blanks, QCs, calibration curve (Completed March 2023)
  Analyze using ESI(-) LC-IMS-MS
  Analyze a subset using CID-MS in (-) and (+)
Perform target screening for 100 PFAS using in-house library and Skyline
Quantify up to 26 PFAS using cal curves in Skyline
Identify non-target suspect PFAS using IM-MS Browser, Mass Profiler, Fluoromatch, and Greg’s proprietary new tool
A
B
C
D
A
B
C
D
Lake Waccamaw
Cape Fear River
Coastal NC
Florida
#C2FFE0
#006600
#800080
#CC9900

## Slide 4: Methods
Generate feature list in Agilent Mass Profiler
  Sites B and C vs method blanks (all 12)
  Sites B and C vs site A (12 random samples)
  MSMS data from sites B and C vs blanks
    Prioritized these for more data reduction and higher confidence IDs
    Once features are identified, go back and look for them in the MS1 only files
Score features using Fluoromatch-IM
Reduce data and prioritize features using Greg’s tool
Investigate features -> did we find any new PFAS?

## Slide 5: Results – Files with MSMS available, BC vs blanks
Focused on gators from sites B and C for NTA, based on target screening data showing highest levels at these sites
Mass Profiler: 2,810 features
Blank subtracted samples by subtracting feature intensities by the mean intensity in the method blank * 3 standard deviations; removed all features with ≤ 0 intensity
After FM-IM and PIMMS: 172 features
Sample | Likely | Tentative (EPA library match) | Tentative (No library match) | Total
1531-91 | 12 | 5 | 20 | 37
1602-91 | 9 | 5 | 8 | 22
1638-91 | 9 | 2 | 11 | 22
1645-91 | 13 | 5 | 16 | 34
2018B-91 | 14 | 6 | 11 | 31
2019B-91 | 12 | 10 | 21 | 43
2019C-91 | 10 | 1 | 16 | 27
2020B-91 | 7 | 7 | 19 | 33
2021B-91 | 9 | 6 | 29 | 44
2022B-91 | 9 | 6 | 21 | 36
2022C-91 | 12 | 2 | 18 | 32
2106-91 | 14 | 4 | 12 | 30
2286-91 | 9 | 2 | 9 | 20
2298-91 | 10 | 6 | 11 | 27
Site B | Likely | Tentative (EPA library match) | Tentative (No library match) | Total
1531-91 | 12 | 5 | 20 | 37
1602-91 | 9 | 5 | 8 | 22
1638-91 | 9 | 2 | 11 | 22
1645-91 | 13 | 5 | 16 | 34
2106-91 | 14 | 4 | 12 | 30
2018B-91 | 14 | 6 | 11 | 31
2019B-91 | 12 | 10 | 21 | 43
2020B-91 | 7 | 7 | 19 | 33
2021B-91 | 9 | 6 | 29 | 44
2022B-91 | 9 | 6 | 21 | 36
Site C | Likely | Tentative (EPA library match) | Tentative (No library match) | Total
2286-91 | 9 | 2 | 9 | 20
2298-91 | 10 | 6 | 11 | 27
2019C-91 | 10 | 1 | 16 | 27
2022C-91 | 12 | 2 | 18 | 32
Sample ID | Season | Location | Sex
1531 | 2018 | B | F
1602 | 2019 | B | M
1638 | 2019 | B | M
1645 | 2019 | B | F
2106 | 2020 | B | M
2286 | 2022 | C | F
2298 | 2022 | C | M

## Slide 6: Results – All features after PIMMS

## Slide 7: Results – More data reduction
Header | Likely | Tentative (EPA library match) | Tentative (No library match)
1531-91 | 12 | 5 | 20
1602-91 | 9 | 5 | 8
1638-91 | 9 | 2 | 11
1645-91 | 13 | 5 | 16
2018B-91 | 14 | 6 | 11
2019B-91 | 12 | 10 | 21
2019C-91 | 10 | 1 | 16
2020B-91 | 7 | 7 | 19
2021B-91 | 9 | 6 | 29
2022B-91 | 9 | 6 | 21
2022C-91 | 12 | 2 | 18
2106-91 | 14 | 4 | 12
2286-91 | 9 | 2 | 9
2298-91 | 10 | 6 | 11
Starting list after PIMMS
Removed all features with RT < 2 min
Likely | Tentative | No match
27 | 24 | 71
Manually cross referenced Baker lab library and removed duplicates from tentative lists
67 prioritized features (tentative and no match) to investigate
Likely | Tentative | No match
27 | 17 | 50

## Slide 8: Results – FM-IM observations
Score | SeriesType_Identifier | Name_or_Class | m/z | Retention Time | row.ID | DT | CCS | Abundance
A | [CF2]n_6 | PFOS-L¦(M-H)-¦NA¦CAS=NA | 498.9302 | 10.45 | 3 | 22.687 | 168.83 | 52951.999
A | [CF2]n_12 | PFOS-L¦(M-H)-¦NA¦CAS=NA | 498.9302 | 10.45 | 3 | 22.687 | 168.83 | 47854.999
A | [CF2]n_5 | PFOS-L¦(M-H)-¦NA¦CAS=NA | 498.9302 | 10.45 | 3 | 22.687 | 168.83 | 43255.999
A | [CF2]n_13 | PFOS-L¦(M-H)-¦NA¦CAS=NA | 498.9302 | 10.45 | 3 | 22.687 | 168.83 | 52869.999
A | [CF2]n_8 | PFOS-L¦(M-H)-¦NA¦CAS=NA | 498.9302 | 10.45 | 3 | 22.687 | 168.83 | 52437.999
A | [CF2]n_7 | PFOS-L¦(M-H)-¦NA¦CAS=NA | 498.9302 | 10.45 | 3 | 22.687 | 168.83 | 52468.999
A | [CF2]n_7 | PFOS-L¦(M-H)-¦NA¦CAS=NA | 498.9302 | 10.45 | 3 | 22.687 | 168.83 | 49764.999
A | [CF2]n_10 | PFOS-L¦(M-H)-¦NA¦CAS=NA | 498.9302 | 10.45 | 3 | 22.687 | 168.83 | 52348.999
A | [CF2]n_8 | PFOS-L¦(M-H)-¦NA¦CAS=NA | 498.9302 | 10.45 | 3 | 22.687 | 168.83 | 52431.999
A | [CF2]n_7 | PFOS-L¦(M-H)-¦NA¦CAS=NA | 498.9302 | 10.45 | 3 | 22.687 | 168.83 | 52353.999
A | [CF2]n_9 | PFOS-L¦(M-H)-¦NA¦CAS=NA | 498.9302 | 10.45 | 3 | 22.687 | 168.83 | 52517.999
PFOS-L (feature ID 3) is placed in 8 different homologous series across the set of 11 samples

## Slide 9: Results – Checking PIMMS in Skyline
Input features into Skyline to quickly check multiple samples at once
Of the 67 features, some were post source decay of multimers of known PFAS – removed from list
Many of them were noise (signal throughout LC gradient) or contamination (peak present in double blank)
15 features remained
Chart: CCS vs m/z of prioritized features post-Skyline
| 349.01409999999998 | 349.01940000000002 | 380.07440000000003 | 181.01609999999999 | 199.0265 | 321.02659999999997 | 165.05520000000001 | 244.90799999999999 | 247.04390000000001 | 301.14510000000001 | 329.04739999999998 | 530.99490000000003 | 223.0292 | 223.0265 | 297.04849999999999
CCS vs m/z | 171.86 | 172.35 | 182.44 | 128.1 | 136.55 | 167.39 | 136.73 | 136.89 | 146.03 | 148.39 | 160.72 | 178.82 | 150.84 | 150.81 | 164.97
Chart: RT vs m/z of prioritized features post-Skyline
| 349.01409999999998 | 349.01940000000002 | 380.07440000000003 | 181.01609999999999 | 199.0265 | 321.02659999999997 | 165.05520000000001 | 244.90799999999999 | 247.04390000000001 | 301.14510000000001 | 329.04739999999998 | 530.99490000000003 | 223.0292 | 223.0265 | 297.04849999999999
RT vs m/z | 4.454 | 4.455 | 2.248 | 3.026 | 4.042 | 4.491 | 5.822 | 6.385 | 7.957 | 9.682 | 9.973 | 11.878 | 14.395 | 14.608 | 14.668

## Slide 10: Results – observation of PIMMS vs Skyline
Feature ID 2288, m/z 165.0552
  PIMMS says only in sample ID 1645
  Skyline says present in all gator samples

## Slide 11: Doesn’t look like anything… back to MS1 data
Sites B and C as experiment, Site A as control for feature prioritization
MP results: 8,958 features
After PIMMS processing: 242 features
  31 likely
  62 tentative (EPA match)
  149 tentative (no EPA match)

## Slide 12: PIMMS output (without any feature validation)
Mean: 16.8 features/gator, SD 9.8
Median: 15.5 features/gator
Min: 1 feature/gator
Max: 47 features/gator

## Slide 13: Breakdown
Site Averages (features/gator)
Total
B 18.5
C 12.0
Likely
B 7.7
C 4.4
Tentative (EPA match)
B 5.0
C 3.4
Tentative (no match)
B 5.8
C 4.2
Site B Averages (Total features/gator)
Season
2018 27.5
2019 17.0
2020 20.7
2021 18.1
2022 17.8
Site C Averages (Total features/gator)
Season
2019 12.9
2022 11.3
Site B Averages (Total features/gator)
Sex
F 20.3
M 17.6
Site C Averages (Total features/gator)
Sex
F 9.3
M 13.3

## Slide 14: Unvalidated PFAS-like features conclusions
More PFAS-like features at site B
No clear trends over time

## Slide 15: Validation of features flagged by PIMMS

## Slide 16: Goals with validation and annotation
Aim of project was using gators as a sentinel species for PFAS exposure
What PFAS are in the gators that should be monitored for in water, fish, and people?
Spreadsheet "C:\Users\Student PC\OneDrive - University of North Carolina at Chapel Hill\UNC Research\2022 Alligator Plasma PFAS\PIMMS\AKB_feature_summary_prioritized_20241204.xlsx“
Prior to validation, all tentative features are Level 5 (62 EPA match + 149 with no match = 211 Level 5 features)

## Slide 17: “Likely” Feature Validation
FM-IM uses a pre-loaded CCS library (based on ours)
PIMMS looks for m/z and CCS matches from FM-IM (score = A) and assigns a “Likely” name
Neither of these check against in-house values for RT -> required for a higher confidence identification
  Without validation, default is Level 3 for these 31 features
  However, Skyline workflow should already catch these features
Goals:
  See if we can find any new PFAS that are isobars of library PFAS
  Investigate how well PIMMS compares to Skyline in alligators

## Slide 18: “Likely” features flagged in PIMMS
31 features matched to 14 different PFAS
  6 PFCAs
    PFNA, PFDA, PFUdA, PFDoA, PFTrDA, PFTeDA
      Can have both M-H- and M-H-CO2-, explains some of the duplicates
  5 PFSAs
    PFHxS, PFHpS, PFOS, PFNS, PFDS
      Library contains L-PFSAs only, so branched isomers are flagged as linear
  3 others
    8:2 FTS
    Nafion Byproduct 2
      Interestingly, 4 features with 3 RT peaks
    PMPA

## Slide 19: “Likely” feature RT checking vs our library
Example of a confirmed match: 8:2 FTS
  Level 1 based on in-house library RT, CCS, and m/z match plus diagnostic evidence (6:2 FTS and 10:2 FTS also detected in Skyline workflow)

## Slide 20: “Likely” feature RT checking vs our library: Erroneous matches
Nafion Byproduct 2 (504, 1086, 2376, 3273)
  RT peaks (8.64, 8.71, 8.78) are seen as 2 peaks in Skyline (8.6 and 8.8 min)
  In house library is 8.8 min
  Skyline also has 2 other peaks (9.2 and 9.4 min) in some samples
  Confirmed the 8.6 and 8.8 min peaks are NBP2 (branched isomers)
    8.8 min: Level 1
    8.6 min: Level 3
  Peaks at 9.2 and 9.4 min could be false negatives in PIMMS or false positives in Skyline (Level 3 or 4?)
PFNA (8367, 330, 3331)
  2 peaks at 10.4 min (matches in house library) – these are confirmed Level 1
  1 peak at 13.2 min with correct CCS for PFNA M-H-CO2-
    Skyline shows several other RTs with this peak – suggests in source fragment of something else
    Several structural possibilities at the same RT could generate a C8F17 in source: heavy N-EtFOSE, heavy N-EtFOSA, 6:8 PFPi)

## Slide 21: “Likely” feature RT checking vs our library: Erroneous matches continued
PFOS (5002) at 10.9 min
  If this is a new PFAS, there’s no way to tell
  More likely just a long tailing PFOS
  Flagged as novel due to no tail in the blanks
  False positive
PFUdA (595, 2130, 377, 747)
  PIMMS has 3 RT peaks (11.7, 11.8, 11.9 min) and 2 CCS peaks
  Skyline has 2 RT peaks: 11.7 and 11.9 min
  Library has 1 RT peak (11.9 min) and 2 CCS peaks (for M-H- and M-H-CO2-)
  595 and 377: confirmed PFUdA
  2130 and 747: br-PFUdA?
PMPA (1413)
  RT of 11.1 min, which does not match our library RT value of 2.6 min
  Skyline also shows a peak at 7.3 min
  More likely in source C3F7O fragment (heavy or native GenX at 7.3 min)
  Possibly indicating some other ether is eluting here (none in our library at a similar RT) – worth investigating more

## Slide 22: “Tentative” PFAS Prioritization
Excluded features with RT < 2 min
  EPA match: 6 features
  No match: 34 features
Imported list to Skyline to check if noise/present in blanks
Investigated remaining features
  Prioritized by highest detection frequency
  Compared to MSMS list

## Slide 23: Imported tentative matches into Skyline
Many of the features were clearly spurious despite being identified in feature finding, FM-IM, and PIMMS filtering
Excluded due to:
  Duplicate of a branched PFSA isomer (PFOS, PFNS, PFDS) -9 features
  Noise present throughout chromatogram -110 features
  Tailing from another feature in m/z or drift dimension -2 features
  Present in high levels in blanks -22 features
Prioritized “tentative” features remaining:
  EPA library match: 13
  No match: 15
Compared prioritized matches to MSMS priority list -> interestingly, no matches
  Could mean no MS2 data available for MS1 priority features? Not necessarily..
Compared priority list to in-house library as a double check
  EPA library matches: 6 of them were post-source decay of a PFCA already in the library
  No match: 9 PSD

## Slide 24: Example: Excluded (present in blanks)
Gator sample
Double blank
Feature ID# 393
PIMMS: Tentative (No library match)
FM-IM: 3+ in RT and DT ordered homologous series
Interestingly, detection frequency with PIMMS was 1.0%
Illustrates complexity of blank subtraction
Suggestion/explore: Use a stricter blank subtraction (e.g. 10x average of blanks)

## Slide 25: Example: Excluded (noise)
Feature ID# 8778
PIMMS: Tentative (EPA library match)
  (1z,6z)-2,2,3,3,4,4,5,5-octafluorohexanediimidamide
FM-IM: Mass defect falling within -0.11 and 0.12 OR exact mass match, and 3+ within homologous series
Detection frequency with PIMMS: 1.0%

## Slide 26: Validation of prioritized “tentative” features
Prioritized “tentative” features remaining:
  EPA library match: 13
  No match: 15
Compared prioritized matches to MSMS priority list -> interestingly, no matches
  Could mean no MS2 data available for MS1 priority features? Not necessarily..
Compared priority list to in-house library as a double check
  EPA library matches: 6 of them were post-source decay of a PFCA already in the library
  No match: 9 PSD

## Slide 27: Example: Post-source decay of something else

## Slide 28: Features that might actually be PFAS
3 “Likely” matches that didn’t line up with in house library values
  2130: matched PFUdA M-H- but lower RT (possible branched isomer)
  747: matched PFUdA M-H-COO- but lower RT (possible branched isomer)
  1413: matched PMPA but wrong RT – possible in source fragment of an ether
7 EPA library matches
  1692: matched PFEESA in the EPA library, but has a different RT than our PFEESA entry
  4751: matched PFECHS in the EPA library, but different CCS than our PFECHS entry
  7712: matched a br-PFOA in the EPA library, likely PFOA M-H- (not in our library)
  2318: matched PubChem CID 22568764 (C8HF17O4S, ether sulfonate)
  6811
  2216
  5135
5 features with no library match
  5849: in series with PFCA M-H-COO-, possibly PFPeDA
  2857: in series with the other PFESAs (1692 and 2318)
  3511
  1159
  331

## Slide 29: Features that might actually be PFAS
3 “Likely” matches that didn’t line up with in house library values
  2130: matched PFUdA M-H- but lower RT (possible branched isomer)
  747: matched PFUdA M-H-COO- but lower RT (possible branched isomer)
  1413: matched PMPA but wrong RT – possible in source fragment of an ether
7 EPA library matches
  1692: matched PFEESA in the EPA library, but has a different RT than our PFEESA entry
  4751: matched PFECHS in the EPA library, but different CCS than our PFECHS entry
  7712: matched a br-PFOA in the EPA library, likely PFOA M-H- (not in our library)
  2318: matched PubChem CID 22568764 (C8HF17O4S, ether sulfonate)
  6811
  2216
  5135
5 features with no library match
  5849: in series with PFCA M-H-COO-, possibly PFPeDA
  2857: in series with the other PFESAs (1692 and 2318)
  3511
  1159
  331

## Slide 30: Long chain PFESAs detected in alligators
Chart: m/z
| 314.93889999999999 | 514.92240000000004 | 564.91869999999994 | 314.93790000000001 | 364.93470000000002 | 414.93150000000003 | 464.92829999999998
 | 166.76 | 172 | 181.89 | 138 | 144.36 | 150.85 | 158.32
Chart: m/z
| 314.93889999999999 | 514.92240000000004 | 564.91869999999994 | 314.93790000000001 | 364.93470000000002 | 414.93150000000003 | 464.92829999999998
 | 11.195 | 10.638 | 11.356 | 6.31 | 7.1 | 8.4 | 9.5
Detected in gators
Detected in SPATTs
Reference standard value in our library
PFHxESA (Feature ID# 2318)
Confidence Level: 2
Molecular Formula: C8HF17O4S
[M-H]-: 514.925131 Da
PFHpESA (Feature ID# 2857)
Confidence Level: 2
Molecular Formula: C9HF19O4S
[M-H]-: 564.921938 Da
Feature ID# 1692
Unidentified. Exact m/z match to PFEESA but wrong RT and wrong CCS

## Slide 31: Features that might actually be PFAS
3 “Likely” matches that didn’t line up with in house library values
  2130: matched PFUdA M-H- but lower RT (possible branched isomer)
  747: matched PFUdA M-H-COO- but lower RT (possible branched isomer)
  1413: matched PMPA but wrong RT – possible in source fragment of an ether
7 EPA library matches
  1692: matched PFEESA in the EPA library, but has a different RT than our PFEESA entry – Level 5
  4751: matched PFECHS in the EPA library, but different CCS than our PFECHS entry
  7712: matched a br-PFOA in the EPA library, likely PFOA M-H- (not in our library)
  2318: matched PubChem CID 22568764 (C8HF17O4S, ether sulfonate). – Level 2
  6811
  2216
  5135
5 features with no library match
  5849: in series with PFCA M-H-COO-, possibly PFPeDA
  2857: in series with the other PFESAs (1692 and 2318) – Level 2
  3511
  1159
  331

## Slide 32: U-PFOS
U-PFOS and PFECHS have the same formula (C8HF15O3S)
Feature 4751 has a different CCS than PFECHS – clearly it is not PFECHS
RT is also a bit different from in-house library RT for PFECHS
U-PFOS has been reported in literature (and SPATTs)
Multiple overlapping RT and DT peaks for this feature
MS2
  PFECHS expected to have a 380.97 fragment
  U-PFOS expected to have unsaturated fragments C3F5 (130.99), C4F7 (180.99), etc.
  Signal not high enough to see any discernable fragments
  Conclusion: U-PFOS, Confidence Level: 3

## Slide 33: Features that might actually be PFAS
3 “Likely” matches that didn’t line up with in house library values
  2130: matched PFUdA M-H- but lower RT (possible branched isomer)
  747: matched PFUdA M-H-COO- but lower RT (possible branched isomer)
  1413: matched PMPA but wrong RT – possible in source fragment of an ether
7 EPA library matches
  1692: matched PFEESA in the EPA library, but has a different RT than our PFEESA entry – Level 5
  4751: matched PFECHS in the EPA library, but different CCS than our PFECHS entry – Level 3
  7712: matched a br-PFOA in the EPA library, likely PFOA M-H- (not in our library)
  2318: matched PubChem CID 22568764 (C8HF17O4S, ether sulfonate). – Level 2
  6811
  2216
  5135
5 features with no library match
  5849: in series with PFCA M-H-COO-, possibly PFPeDA
  2857: in series with the other PFESAs (1692 and 2318) – Level 2
  3511
  1159
  331

## Slide 34: PFOA M-H- post source decay
PFOA M-H- is not in our library currently
Feature exactly matches PFOA M-H- m/z and aligns with our library RT value
PFOA M-H-CO2- drift window
PFOA M-H- drift window
PFOA multimer drift window
PFOA M-H-CO2- m/z
13C8-PFOA M-H-CO2- m/z
PFOA M-H-
m/z
13C8-PFOA M-H-
m/z
Conclusion: duplicate identification of PFOA

## Slide 35: Features that might actually be PFAS
3 “Likely” matches that didn’t line up with in house library values
  2130: matched PFUdA M-H- but lower RT (possible branched isomer)
  747: matched PFUdA M-H-COO- but lower RT (possible branched isomer)
  1413: matched PMPA but wrong RT – possible in source fragment of an ether
7 EPA library matches
  1692: matched PFEESA in the EPA library, but has a different RT than our PFEESA entry – Level 5
  4751: matched PFECHS in the EPA library, but different CCS than our PFECHS entry – Level 3
  7712: matched a br-PFOA in the EPA library, likely PFOA M-H- (not in our library) - na
  2318: matched PubChem CID 22568764 (C8HF17O4S, ether sulfonate). – Level 2
  6811
  2216
  5135
5 features with no library match
  5849: in series with PFCA M-H-COO-, possibly PFPeDA
  2857: in series with the other PFESAs (1692 and 2318) – Level 2
  3511
  1159
  331

## Slide 36: Not PMPA
Feature 1413 (m/z 184.985) matched PMPA in the EPA library
CCS values match almost exactly
RT values are very different (PMPA in library = 2.6 min)
Enough evidence to propose a formula (C3F7O)
However, RT makes no sense
Hypothesis: this is an in source fragment of another ether
HFPO-DA (GenX)
(or SIL)
HFPO-TrA
HFPO-TeA

## Slide 37: Not PMPA
HFPO-DA (GenX)
(or SIL)
HFPO-TrA
HFPO-TeA
None of the native precursors were detected in any sample
Heavy GenX was detected broadly – internal standard spike (likely the peak at 7.3 is from the IS)
Next step: do a correlation analysis of this feature based on location/year, looking at the last 3 peaks only
Hypothesis: expecting to see more peaks in Site B vs Site A, and more in 2018 than in later years
No matching PFECAs in our library with this RT

## Slide 38: Features that might actually be PFAS
3 “Likely” matches that didn’t line up with in house library values
  2130: matched PFUdA M-H- but lower RT (possible branched isomer)
  747: matched PFUdA M-H-COO- but lower RT (possible branched isomer)
  1413: matched PMPA but wrong RT – possible in source fragment of an ether - TBD
7 EPA library matches
  1692: matched PFEESA in the EPA library, but has a different RT than our PFEESA entry – Level 5
  4751: matched PFECHS in the EPA library, but different CCS than our PFECHS entry – Level 3
  7712: matched a br-PFOA in the EPA library, likely PFOA M-H- (not in our library) - na
  2318: matched PubChem CID 22568764 (C8HF17O4S, ether sulfonate). – Level 2
  6811
  2216
  5135
5 features with no library match
  5849: in series with PFCA M-H-COO-, possibly PFPeDA
  2857: in series with the other PFESAs (1692 and 2318) – Level 2
  3511
  1159
  331

## Slide 39: PFPeDA
PFPeDA
M-H- CCS: 218.72
M-H-CO2 CCS: 197
RT: 13.7 min
PFPeDA, Confidence Level 2

## Slide 40: Features that might actually be PFAS
3 “Likely” matches that didn’t line up with in house library values
  2130: matched PFUdA M-H- but lower RT (possible branched isomer)
  747: matched PFUdA M-H-COO- but lower RT (possible branched isomer)
  1413: matched PMPA but wrong RT – possible in source fragment of an ether - TBD
7 EPA library matches
  1692: matched PFEESA in the EPA library, but has a different RT than our PFEESA entry – Level 5
  4751: matched PFECHS in the EPA library, but different CCS than our PFECHS entry – Level 3
  7712: matched a br-PFOA in the EPA library, likely PFOA M-H- (not in our library) - na
  2318: matched PubChem CID 22568764 (C8HF17O4S, ether sulfonate). – Level 2
  6811: m/z 480.968 (plus 2 isobars at different RTs)
  2216: matched formula C11H10F4O4
  5135: m/z 448.966, matched formula C8H3F17Si
5 features with no library match
  5849: in series with PFCA M-H-COO-, possibly PFPeDA – Level 2
  2857: in series with the other PFESAs (1692 and 2318) – Level 2
  3511: m/z 207.0420
  1159: m/z 229.0550
  331: m/z 323.09

## Slide 41: 2130 and 747 – PFUdA?
IS signal predominates at 11.9 min
No IS signal at 11.7 min
MS2 fragments
M-H-CO2: 168.9931 (C3F7), 118.9934 (C2F5)
MS2 fragments
M-H-CO2: 318.9974 (C6F13), 218.9856 (C4F9), 168.9931 (C3F7), 118.9934 (C2F5)
Conclusion:
Peak at 11.7 is br-PFUdA, confidence level 3
PIMMS matched Likely PFUdA for a signal at 11.7 min

## Slide 42: Features that might actually be PFAS
3 “Likely” matches that didn’t line up with in house library values
  2130: matched PFUdA M-H- but lower RT (possible branched isomer) – Level 3
  747: matched PFUdA M-H-COO- but lower RT (possible branched isomer) – Level 3
  1413: matched PMPA but wrong RT – possible in source fragment of an ether - TBD
7 EPA library matches
  1692: matched PFEESA in the EPA library, but has a different RT than our PFEESA entry – Level 5
  4751: matched PFECHS in the EPA library, but different CCS than our PFECHS entry – Level 3
  7712: matched a br-PFOA in the EPA library, likely PFOA M-H- (not in our library) - na
  2318: matched PubChem CID 22568764 (C8HF17O4S, ether sulfonate). – Level 2
  6811: m/z 480.968 (plus 2 isobars at different RTs)
  2216: matched formula C11H10F4O4
  5135: m/z 448.966, matched formula C8H3F17Si
5 features with no library match
  5849: in series with PFCA M-H-COO-, possibly PFPeDA – Level 2
  2857: in series with the other PFESAs (1692 and 2318) – Level 2
  3511: m/z 207.0420
  1159: m/z 229.0550
  331: m/z 323.09

## Slide 43: 5135 – m/z 448.9655
PIMMS matched EPA library for (Heptadecafluorooctyl)silane C8H3F17Si – seems unlikely
No Baker library matches
Drift aligned peak at m/z 592.9495 seen in all of the same peaks and all the same samples
Post source decay of the m/z 592 feature, or its own thing?
448.9655 + CO2C2F4 = 592.9495
Chart: EICs of coeluting gator features
| 10.759 | 10.776999999999999 | 10.795 | 10.813000000000001 | 10.831 | 10.849 | 10.867000000000001 | 10.885 | 10.901999999999999 | 10.92 | 10.938000000000001 | 10.956 | 10.974 | 10.992000000000001 | 11.01 | 11.026999999999999 | 11.045 | 11.063000000000001 | 11.081 | 11.099 | 11.117000000000001
592.9481 | 1566 | 3707 | 5033 | 6074 | 7863 | 7994 | 5955 | 4371 | 6334 | 11049 | 13710 | 10355 | 5206 | 3872 | 11272 | 22737 | 26474 | 20022 | 9412 | 3445 | 276
448.9647 | 646 | 1399 | 2116 | 2333 | 3488 | 3271 | 2149 | 1129 | 1278 | 3675 | 4641 | 3860 | 2126 | 1672 | 5386 | 9681 | 11897 | 9819 | 4554 | 830 | 195

## Slide 44: Other possible structures for m/z 592.9481
Backbone of compounds 9 & 10. Kaylie’s paper suggested the H-substitution for the carboxylic acid group is plausible and reported elsewhere
m/z 282.9822
m/z 262.9760
Identification: H-substituted perfluoro triether carboxylic acid
Confidence level: 3
Novel PFAS

## Slide 45: Other possible structure for m/z 592.9495
448.9655 + CO2C2F4 = 592.9495 <- Evidence: These are drift aligned and RT aligned. Could suggest that 592 has a carboxylic acid group attached to a C2F4
Observed fragments:
  262.9755 = C5F9O2
  212.9787 = C4F7O2
  184.9837 = C3F7O2
  168.9888 = C3F7
  118.9920 = C2F5
  79.9593 = SO3 (however – this feature coelutes with PFNS and is close in drift time, so there might not necessarily be an SO3 here)
Possible formula for 448.9655: C5F9O2 + C3F7O + H
Multiple RT peaks suggests multiple branched forms
Possible molecular formula: C11H2F20O5
  Exactly one PubChem CID (163325041) matches formula but structure doesn’t line up with a CO2(CF2)2 loss
Identification: H-substituted perfluoro triether carboxylic acid
Confidence level: 3
Novel PFAS
m/z 448.9655

## Slide 46: m/z 450.9280 and 414.9492
Nested spectra for peak at 11.0 min (m/z 450.9273, not seen at lower RTs)
Also seeing feature at m/z 414.9492 eluting at 11.0 min only and close but not quite drift aligned with both 448 and 450!
What is going on here?!
For now – considering a likely in-source decay product of m/z 592.9481, formula TBD
Chart: EICs of coeluting gator features
| 10.759 | 10.776999999999999 | 10.795 | 10.813000000000001 | 10.831 | 10.849 | 10.867000000000001 | 10.885 | 10.901999999999999 | 10.92 | 10.938000000000001 | 10.956 | 10.974 | 10.992000000000001 | 11.01 | 11.026999999999999 | 11.045 | 11.063000000000001 | 11.081 | 11.099 | 11.117000000000001
592.9481 | 1566 | 3707 | 5033 | 6074 | 7863 | 7994 | 5955 | 4371 | 6334 | 11049 | 13710 | 10355 | 5206 | 3872 | 11272 | 22737 | 26474 | 20022 | 9412 | 3445 | 276
448.9647 | 646 | 1399 | 2116 | 2333 | 3488 | 3271 | 2149 | 1129 | 1278 | 3675 | 4641 | 3860 | 2126 | 1672 | 5386 | 9681 | 11897 | 9819 | 4554 | 830 | 195
414.9479 | 1333 | 17217 | 66007 | 124822 | 152713 | 124640 | 67696 | 25885 | 6878 | 1535 | 0 | 123
Chart: EICs of coeluting gator features
| 10.956 | 10.974 | 10.992000000000001 | 11.01 | 11.026999999999999 | 11.045 | 11.063000000000001 | 11.081 | 11.099 | 11.117000000000001 | 11.135 | 11.151999999999999 | 11.17 | 11.188000000000001 | 11.206 | 11.224
450.9259 | 228 | 13023 | 86222 | 277173 | 529129 | 643991 | 533143 | 292073 | 113542 | 34049 | 10146 | 3199 | 730 | 72 | 172 | 159
414.9479 | 1333 | 17217 | 66007 | 124822 | 152713 | 124640 | 67696 | 25885 | 6878 | 1535 | 0 | 123
Drift pattern suggests carboxylic acid (in source dimer)

## Slide 47: m/z 628.9189
Kaylie’s compound 10 with loss of a COOH
Compound 10 not detected in gators
Other possible structural isomer
Fragments: 262.9749
Chart: EICs of close eluting gator features
| 10.706 | 10.724 | 10.742000000000001 | 10.759 | 10.776999999999999 | 10.795 | 10.813000000000001 | 10.831 | 10.849 | 10.867000000000001 | 10.885 | 10.901999999999999 | 10.92 | 10.938000000000001 | 10.956 | 10.974 | 10.992000000000001 | 11.01 | 11.026999999999999 | 11.045 | 11.063000000000001 | 11.081 | 11.099 | 11.117000000000001
628.9148 | 4483 | 17414 | 33464 | 40248 | 45194 | 51294 | 55065 | 44747 | 31032 | 32919 | 41958 | 40747 | 24835 | 11008 | 14737 | 41364 | 69341 | 70567 | 48103 | 20620 | 9241 | 5031 | 2947 | 1090
592.9481 | 1566 | 3707 | 5033 | 6074 | 7863 | 7994 | 5955 | 4371 | 6334 | 11049 | 13710 | 10355 | 5206 | 3872 | 11272 | 22737 | 26474 | 20022 | 9412 | 3445 | 276
No Pubchem entries match this formula – novel PFAS
Perfluorinated ether sulfonic acid
C10H2F20O6S M-H-
Confidence level: 3
Kaylie’s compound 10 with loss of a COOH
Compound 10 not detected

## Slide 48: Conclusions from feature ID 5135
PIMMS flagged one feature (m/z 448.966) as matching formula C8H3F17Si on the EPA list
Manual validation confirmed a different formula (C8HF16O3)
  Calling this a Level 3 even though it might be an in source fragment of m/z 592.9495
Further investigation found 4 additional features
  m/z 592.9495 – tentative structure proposed
  m/z 628.9189 – tentative structure proposed
  m/z 450.9280 – no formula yet, likely in source fragment of m/z 592.9495
  m/z 414.9492 – no formula yet, likely in source fragment of m/z 592.9495
One feature flagged resulted in…
  3 features ID’ed to Confidence Level 3 (all novel)
  2 features ID’ed to Confidence Level 5

## Slide 49: Features that might actually be PFAS
3 “Likely” matches that didn’t line up with in house library values
  2130: matched PFUdA M-H- but lower RT (possible branched isomer) – Level 3
  747: matched PFUdA M-H-COO- but lower RT (possible branched isomer) – Level 3
  1413: matched PMPA but wrong RT – possible in source fragment of an ether - TBD
7 EPA library matches
  1692: matched PFEESA in the EPA library, but has a different RT than our PFEESA entry – Level 5
  4751: matched PFECHS in the EPA library, but different CCS than our PFECHS entry – Level 3
  7712: matched a br-PFOA in the EPA library, likely PFOA M-H- (not in our library) - na
  2318: matched PubChem CID 22568764 (C8HF17O4S, ether sulfonate). – Level 2
  6811: m/z 480.968 (plus 2 isobars at different RTs)
  2216: matched formula C11H10F4O4
  5135: m/z 448.966, matched formula C8H3F17Si – 3 Level 3s, 2 Level 5s
5 features with no library match
  5849: in series with PFCA M-H-COO-, possibly PFPeDA – Level 2
  2857: in series with the other PFESAs (1692 and 2318) – Level 2
  3511: m/z 207.0420
  1159: m/z 229.0550
  331: m/z 323.09

## Slide 50: 6811 – m/z 480.9680
PIMMS found m/z 480.9680 (EPA match to formula C12H2F16O2) , CCS 165.79, RT 10.54
  While validating features, found it to be present in blanks
  Conclusion: contamination
However, looking in Skyline, there appeared to be a tailing peak from the PIMMS feature at a slightly lower m/z that was appearing at 2 different RTs
  m/z 480.937
    10.2 min, CCS 165.4
    9.7 min, CCS 159.5
  Exact mass matches formula C8HF16O3S (1H-substituted PFOS)
  Fragmentation spectra show SO3 and SO3F fragments
  However, drift and RT overlaps with PFOS-br so these are not diagnostic
  Abundance is too low to get meaningful fragments
Conclusion: Confidence Level 5

## Slide 51: Features that might actually be PFAS
3 “Likely” matches that didn’t line up with in house library values
  2130: matched PFUdA M-H- but lower RT (possible branched isomer) – Level 3
  747: matched PFUdA M-H-COO- but lower RT (possible branched isomer) – Level 3
  1413: matched PMPA but wrong RT – possible in source fragment of an ether - TBD
7 EPA library matches
  1692: matched PFEESA in the EPA library, but has a different RT than our PFEESA entry – Level 5
  4751: matched PFECHS in the EPA library, but different CCS than our PFECHS entry – Level 3
  7712: matched a br-PFOA in the EPA library, likely PFOA M-H- (not in our library) - na
  2318: matched PubChem CID 22568764 (C8HF17O4S, ether sulfonate). – Level 2
  6811: m/z 480.968 (plus 2 isobars at different RTs) – 2 Level 5s
  2216: matched formula C11H10F4O4
  5135: m/z 448.966, matched formula C8H3F17Si – 3 Level 3s, 2 Level 5s
5 features with no library match
  5849: in series with PFCA M-H-COO-, possibly PFPeDA – Level 2
  2857: in series with the other PFESAs (1692 and 2318) – Level 2
  3511: m/z 207.0420
  1159: m/z 229.0550
  331: m/z 323.09

## Slide 52: 2216: m/z 281.0429
EPA library match to C11H10F4O4
Fragments: 237.0565
Low signal though and very low precursor signal

## Slide 56: Conclusions from feature validation

## Slide 57: What does it all mean?

## Slide 58: Back to Skyline
Relative abundance comparisons of all features in our library and those ID’ed with PIMMS
  Group by: absolute quant, other Level 1, Level 2, Level 3, Level 4, Level 5
  Unique aspect of IMS+PFAS is greater likelihood that Level 4 and 5 features are actually the same features across samples

## Slide 59: Overall conclusions

## Slide 60: Future directions
Adding dimers and post-source decay to library will help reduce false positives with less manual validation
Try different sample prep protocols (add formic acid) to see if it boosts signal – could improve MS2 fragmentation spectra
Monitor these PFAS in people from this area