## Slide 1: Alligator PFAS Study: Non-Targeted Analysis
December 2024

## Slide 2: Experimental Design
Extract 200 plasma samples along with blanks, QCs, calibration curve (Completed March 2023)
  Analyze using ESI(-) LC-IMS-MS
  Analyze a subset using CID-MS in (-) and (+)
Perform target screening for 100 PFAS using in-house library and Skyline
Quantify up to 26 PFAS using cal curves in Skyline
Identify non-target suspect PFAS using IM-MS Browser, Mass Profiler, Fluoromatch, and Greg’s proprietary new tool
A
B
C
D
A
B
C
D
Lake Waccamaw
Cape Fear River
Coastal NC
Florida
#C2FFE0
#006600
#800080
#CC9900

## Slide 3: Methods
Generate feature list in Agilent Mass Profiler
Score features using Fluoromatch-IM
Reduce data and prioritize features using Greg’s tool
Investigate features -> did we find any new PFAS?
Compare feature abundance and detections over time at each site

## Slide 4: Results: Feature finding and initial prioritization
MassProfiler results: 8,958 features
After processing with Greg’s tool: 242 features
  31 “likely” (m/z and CCS match to library)
  62 tentative with an m/z match to EPA library
  149 tentative, no library match

## Slide 5: Descriptive statistics of unvalidated features
Mean: 16.8 features/gator, SD 9.8
Median: 15.5 features/gator
Min: 1 feature/gator
Max: 47 features/gator

## Slide 6: Validation of PFAS-like features

## Slide 7: Additional processing and feature prioritization
Excluded all features that matched m/z, CCS, and RT of a PFAS already in our library
Excluded all features with RT < 2 min
Excluded noisy features and those present in blanks (visually checked all relevant samples and blanks by loading feature list into Skyline)
14 features remained and were manually annotated
  2 features (ID# 2130 and 747): br-PFUdA (M-H- and M-H-CO2-), level 3 confidence
  1 feature (ID# 5849): PFPeDA, level 2 confidence
  1 feature (ID# 4751): U-PFOS, level 3 confidence
  7 features (ID# 1413, 1692, 6811, 2216, 3511, 1159, 331): Not ID’ed, level 5 confidence
  2 features (ID# 2318 and 2857): New additions to PFEESA homologous series, PFHxESA and PFHpESA, level 2 confidence
  1 feature (ID# 5135): Investigation resulted in 3 novel PFAS (level 3 confidence) and 2 additional features of interest (level 5 confidence)

## Slide 8: Long chain PFESAs detected in alligators
Chart: m/z
| 314.93889999999999 | 514.92240000000004 | 564.91869999999994 | 314.93790000000001 | 364.93470000000002 | 414.93150000000003 | 464.92829999999998
 | 166.76 | 172 | 181.89 | 138 | 144.36 | 150.85 | 158.32
Chart: m/z
| 314.93889999999999 | 514.92240000000004 | 564.91869999999994 | 314.93790000000001 | 364.93470000000002 | 414.93150000000003 | 464.92829999999998
 | 11.195 | 10.638 | 11.356 | 6.31 | 7.1 | 8.4 | 9.5
Detected in gators
Detected in SPATTs
Reference standard value in our library
PFHxESA (Feature ID# 2318)
Confidence Level: 2
Molecular Formula: C8HF17O4S
[M-H]-: 514.925131 Da
PFHpESA (Feature ID# 2857)
Confidence Level: 2
Molecular Formula: C9HF19O4S
[M-H]-: 564.921938 Da
Feature ID# 1692
Confidence level: 5
Unidentified
Exact m/z match to PFEESA, wrong RT, wrong CCS

## Slide 9: Feature ID# 5135 – m/z 448.9655
m/z 282.9822
m/z 262.9760
MS2 Fragments:
Identification: H-substituted polyfluoroether alcohol?
Confidence level: 3
Novel PFAS? (see next slide…)

## Slide 10: m/z 592.959 drift aligned with feature ID# 5135
Strong correlation in peak areas of these two features
448.9655 + CO2C2F4 = 592.9495
Chart: EICs of coeluting gator features
| 10.759 | 10.776999999999999 | 10.795 | 10.813000000000001 | 10.831 | 10.849 | 10.867000000000001 | 10.885 | 10.901999999999999 | 10.92 | 10.938000000000001 | 10.956 | 10.974 | 10.992000000000001 | 11.01 | 11.026999999999999 | 11.045 | 11.063000000000001 | 11.081 | 11.099 | 11.117000000000001
592.9481 | 1566 | 3707 | 5033 | 6074 | 7863 | 7994 | 5955 | 4371 | 6334 | 11049 | 13710 | 10355 | 5206 | 3872 | 11272 | 22737 | 26474 | 20022 | 9412 | 3445 | 276
448.9647 | 646 | 1399 | 2116 | 2333 | 3488 | 3271 | 2149 | 1129 | 1278 | 3675 | 4641 | 3860 | 2126 | 1672 | 5386 | 9681 | 11897 | 9819 | 4554 | 830 | 195
Identification: H-substituted polyfluoroether alcohol
Confidence level: 3
Novel PFAS
Post source decay of m/z 592.9495?
Metabolite of m/z 592.9495?
m/z 592.9495
m/z 448.9677
Chart: Peak area of m/z 592.9495

## Slide 11: Possible structures for m/z 592.9481
Identification: H-substituted perfluoro triether carboxylic acid
Confidence level: 3 (fragments cannot distinguish between isomers)
Novel PFAS
Comparison to novel SPATT compounds:
  m/z 448.9676 observed as a fragment of compounds 9 & 10 (multi-headed perfluorinated ethers)
  Kaylie’s paper suggested that an H-substitution of a carboxylic acid group is plausible and has been reported elsewhere, though that wasn’t detected in the SPATTs

## Slide 12: m/z 628.9189
Kaylie’s compound 10 with loss of a COOH
Compound 10 not detected in gators
Another possible structural isomer
Chart: EICs of close eluting gator features
| 10.706 | 10.724 | 10.742000000000001 | 10.759 | 10.776999999999999 | 10.795 | 10.813000000000001 | 10.831 | 10.849 | 10.867000000000001 | 10.885 | 10.901999999999999 | 10.92 | 10.938000000000001 | 10.956 | 10.974 | 10.992000000000001 | 11.01 | 11.026999999999999 | 11.045 | 11.063000000000001 | 11.081 | 11.099 | 11.117000000000001
628.9148 | 4483 | 17414 | 33464 | 40248 | 45194 | 51294 | 55065 | 44747 | 31032 | 32919 | 41958 | 40747 | 24835 | 11008 | 14737 | 41364 | 69341 | 70567 | 48103 | 20620 | 9241 | 5031 | 2947 | 1090
592.9481 | 1566 | 3707 | 5033 | 6074 | 7863 | 7994 | 5955 | 4371 | 6334 | 11049 | 13710 | 10355 | 5206 | 3872 | 11272 | 22737 | 26474 | 20022 | 9412 | 3445 | 276
No Pubchem entries match this formula
Perfluorinated ether sulfonic acid
C10H2F20O6S M-H-
Confidence level: 3
Novel PFAS
Fragments: 282.9931, 262.9749 118.9707, 82.9619

## Slide 13: Additional features m/z 450.9280 and 414.9492
Nested spectra for peak at 11.0 min (m/z 450.9273)
While investigating m/z 592.9481, observed a close eluting peak at m/z 450.9259
While looking into it, also saw a feature at m/z 414.9492 eluting at 11.0 min and drift aligned with 450!
What is going on here?!
Are these the same molecule or different?
Chart: EICs of coeluting gator features
| 10.759 | 10.776999999999999 | 10.795 | 10.813000000000001 | 10.831 | 10.849 | 10.867000000000001 | 10.885 | 10.901999999999999 | 10.92 | 10.938000000000001 | 10.956 | 10.974 | 10.992000000000001 | 11.01 | 11.026999999999999 | 11.045 | 11.063000000000001 | 11.081 | 11.099 | 11.117000000000001
592.9481 | 1566 | 3707 | 5033 | 6074 | 7863 | 7994 | 5955 | 4371 | 6334 | 11049 | 13710 | 10355 | 5206 | 3872 | 11272 | 22737 | 26474 | 20022 | 9412 | 3445 | 276
448.9647 | 646 | 1399 | 2116 | 2333 | 3488 | 3271 | 2149 | 1129 | 1278 | 3675 | 4641 | 3860 | 2126 | 1672 | 5386 | 9681 | 11897 | 9819 | 4554 | 830 | 195
414.9479 | 1333 | 17217 | 66007 | 124822 | 152713 | 124640 | 67696 | 25885 | 6878 | 1535 | 0 | 123
Chart: EICs of coeluting gator features
| 10.956 | 10.974 | 10.992000000000001 | 11.01 | 11.026999999999999 | 11.045 | 11.063000000000001 | 11.081 | 11.099 | 11.117000000000001 | 11.135 | 11.151999999999999 | 11.17 | 11.188000000000001 | 11.206 | 11.224
450.9259 | 228 | 13023 | 86222 | 277173 | 529129 | 643991 | 533143 | 292073 | 113542 | 34049 | 10146 | 3199 | 730 | 72 | 172 | 159
414.9479 | 1333 | 17217 | 66007 | 124822 | 152713 | 124640 | 67696 | 25885 | 6878 | 1535 | 0 | 123
Isotopic pattern suggests Br or multiple Cl
Fragments aligned with m/z 414.9492

## Slide 14: m/z 450.9280 structural elucidation
Weed et al. https://doi.org/10.3390/toxics12060403

## Slide 15: Feature ID# 1413: Not PMPA
HFPO-DA (GenX)
(or SIL)
HFPO-TrA
HFPO-TeA
m/z 184.985 and CCS 115.2 matched our library entry for PMPA, but RT should be 2.6 min
No matching PFECAs in our library with this RT
Multiple drift peaks indicates multimerization -> characteristic of ethers and carboxylic acids on our platform
Hypothesis: This is an in-source fragment of an undetected PFECA
Can we call this a Level 5?

## Slide 16: Summary 1/2
2 previously-unreported (I think) PFAESAs (in homologous series with PFEESA)
2 novel PFAS (no matches in PubChem)
PFHxESA (Feature ID# 2318)
Confidence Level: 2
Molecular Formula: C8HF17O4S
[M-H]-: 514.925131 Da
PFHpESA (Feature ID# 2857)
Confidence Level: 2
Molecular Formula: C9HF19O4S
[M-H]-: 564.921938 Da
H-substituted polyfluorinated triether carboxylic acid
Confidence Level: 3
Molecular Formula: C11H2F20O5
[M-H]-: 592.9510 Da
H-substituted polyfluorinated triether sulfonic acid
Confidence Level: 3
Molecular Formula: C10H2F20O6S
[M-H]-: 628.9180 Da

## Slide 17: Summary 2/2
1 fluorinated insecticide
1 indication of an ether with no ether detected
2 PFAS that might be in source fragments or their own things
Fipronil sulfone
Confidence Level: 2
Molecular Formula: C12H4O2N4Cl2F3S
[M-H]-: 450.9258 Da
Undetected PFECA
Confidence Level: 5
Molecular Formula: C3F7O + R
[M-H]-: TBD
Feature ID# 1692
Confidence level: 5
Unidentified
Exact m/z match to PFEESA, wrong RT, wrong CCS
Feature ID# 5135
Confidence level: 3
Molecular formula: C8H2F16O3
[M-H]-: 448.9655
Drift aligned and perfectly coelutes with m/z 592.9495

## Slide 18: Next steps
Decide how to report the possible in source fragments
Get relative abundances of all features (in our library and the novel ones) in Skyline
Explore site and year trends
Identify remaining features (if possible)
Write

## Slide 19: Initial comparison of feature abundances (new PFAS only)
Clear separation of sites B and C from each other and from A and D

## Slide 20: Site trends
C3F7O-
m/z 628.92
Fipronil sulfone
m/z 448.97
m/z 592.95
PFHpESA
PFHxESA
PFHpESA isomer
PFHxESA isomer
A (Lake Waccamaw)
B (Cape Fear)
C (Coastal NC)
D (Florida)
H-substituted polyfluoro triethers
Highest abundance in coastal animals
Long chain PFAESAs
Higher abundance in CFR animals

## Slide 21: Sites A and B time trends